## Slide 1: Bamboo can be used to make cricket bats
Teacher Guide
Curriculum links: Properties of materials & their uses
Suitable: 7-11 years

## Slide 2: Bamboo can be used to make cricket bats
Subject knowledge
Enquiry skills*
Understand that the properties of a material determine whether it suitable for a particular use
Understand that sometimes, the way that humans use natural resources is unsustainable
Cricket bats have been made of willow for almost 200 years. However, there is now a shortage of high-quality willow and an unsustainable demand for willow worldwide. Scientists have been comparing other materials with similar properties to see if there is an alternative material that can be used. Children will learn about the properties of willow and bamboo and how these properties can be tested and compared.
Children measure and compare the bounciness of different surfaces using one type of hard ball, or the bounciness of different balls against a hard surface.
Summary of science research
Related investigations for children
Notes: *We recommend that you focus on one of these enquiry skills when children carry out one of the research-related investigations.
Of course, you might like to choose a different focus:
Asking questions
Making predictions
Observing and measuring
Recording data
Evaluating

## Slide 3: Key vocabulary
bamboo - a type of grass with a similar structure to wood
cell - the smallest unit that can live on its own, they make up all living organisms
coefficient of restitution - a measure of the speed that two objects move apart after hitting each other
collided - to crash into, or hit, another object
compress/compression - a force that squeezes something together
damping - a process that stops something vibrating
deformed - to make something have a new shape by twisting, pushing or pulling it
density - a measure of how much material is packed into a certain space
elastic - the ability of a deformed material to return to its original size and shape when the forces causing the change in shape are removed
energy - the ability to do work, energy can be stored or transferred from one thing to another
flexibility - the ability of a material to bend and return to its original shape
hardness - a measure of how hard a material is
material - a substance that something is made of
properties - describes what the material is like/can do, e.g., hard, smooth, strong
resin - thick, sticky liquid substance
sustainable - the idea that humans must interact with the environment in a way that means there will be enough resources left for future generations
unsustainable - there is no way to keep doing something at the same rate or in the same way, e.g. some human activities use natural resources more quickly that they can be replaced
vibrating - very quickly moving back and forth or up and down
willow - a type of tree
Notes: Notes for teachers

## Slide 4: Quick activity
What do you think this is?
Notes: Have a range of sticky objects to show children.
As well as glues and adhesive tapes, don’t forget Velcro on shoes, string, laces, envelopes, post it notes, etc.
Think – pair - share

## Slide 5: What did the scientists know about cricket bats?
Cricket bats are made from willow.
What properties does a cricket bat have?
The scientists had a background of playing cricket and understood what properties a cricket bat has to have.
© THUGCHILDz*
Notes: Teachers may like to have a cricket bat, some objects made from willow (e.g. baskets) and bamboo (e.g. garden canes, bowls, clothing) to show the children.
Key information
Cricket bats must be hard, smooth and strong.
Cricket bats are made from willow.
There aren’t enough willow trees in the world to keep making cricket bats.
Bamboo is already used for many different purposes.
Bamboo is a grass (not a tree). Many of the larger woody bamboo species are very tree-like in appearance and can be called ‘bamboo trees’.
The scientists like playing cricket and understood what properties a cricket bat has to have.
Materials can be natural or artificial – wood is a natural material.
Some natural materials will run out one day (unsustainable) - willow trees take at least 6 years to mature, and often closer to 15 years before the willow is ready to be used. This has led to a widespread shortage in high quality willow to make crickets bats (and an unsustainable demand for willow worldwide).
Questions to ask the children
Can you describe the properties of a cricket bat? Encourage children to describe the properties, e.g. hard, smooth, stiff (rigid), strong. Make children aware that a ricket bat is made of willow (a type of wood).
*© THUGCHILDc, Licenced through Creative Commons and accessed here - https://commons.wikimedia.org/wiki/File:Bat(cricket).jpg

## Slide 6: What did the scientists know about willow and bamboo?
Global supplies of willow are becoming unsustainable.
Bamboo is a highly sustainable and versatile material that is used for many different purposes.
© Willow*
What other uses does bamboo have?
Notes: Questions to ask the children
Where does willow come from? Look at the image of the willow tree. Maybe go outside to see if you can find a willow tree growing nearby. Explain that willow is a natural material.
What does unsustainable mean? can’t last forever, an unsustainable resource is used up and can’t be replaced
Why is willow unsustainable? Willow trees take at least 6 years to mature, and often closer to 15 years before the willow is ready to be used. This has led to a widespread shortage in high quality willow to make crickets bats, and an unsustainable demand for willow worldwide.
Can you think of any other materials where global demand is unsustainable? Children could research this. Examples are oil, gas, coal, etc.
What is bamboo used for? Look at some bamboo objects. Encourage the children to describe the properties of the bamboo.
Where does bamboo come from? Look at images of bamboo. Children may have seen bamboo garden canes but not realised that they come from a plant. Explain that this is a natural material.
Can you think of other products bamboo could be used for in the future?
Why do you think bamboo is such a good sustainable material? Bamboo is fast-growing and cheap.
*© Willow, Licenced through Creative Commons and accessed here - https://commons.wikimedia.org/wiki/File:Salix_alba_013.jpg

## Slide 7: What did the scientists do?
The scientists made a bamboo bat.
They tested the bamboo bat and a willow bat to find out:
how squashy the bat was
how bendy the bat was
how hard the bat was
how shaky the bat was
how bouncy the bat was
Why do you think it was necessary to perform different tests on the bats?
A compression machine is used to test how much a material can be squashed by a force pressing down on it.
© Cjp24*
Notes: Question to ask children:
Why do you think it was necessary to perform different tests on the bats?
To be useful, the cricket bat must have many different properties – to be strong (not squashy), stiff (not bendy), hard, and pleasant to use (not shaking or bouncy).
Background information (for teachers)
Compression – how much the bat could be squashed
Flexibility – how bendy the bat was
Hardness – how hard the material was
Damping – how quickly vibrations stopped
Coefficient of Restitution – how bouncy the material was
Compression – tested by using heavy weights, about 10,000kg, to ‘squash’ the material whilst filming it to determine the point, and method, of breaking. Compression testing also gives a value for a measure called the Modulus of Elasticity (MoE) – basically how easily the material can be deformed. Think about squeezing a piece of plasticine which changes shape easily, low MoE, compared to trying to squeeze a piece of wood that doesn’t change shape, high MoE.
Flexibility – measured by bending the bat at different points along its length until it breaks.
Hardness – measured using the Vickers-Hardness Test, this involves pressing a pyramid-shaped diamond onto the surface of the material using a precise force. The area of the dent left by the diamond is then measured.
Damping – measure of how quickly a material stops vibrating after being struck by a hard object. It is measured by using a sensitive microphone to listen for vibrations in the material.
Coefficient of Restitution (CoR) – a measure of the speed that 2 objects move apart after they have collided. Think about a bouncy ball hitting a hard floor and bouncing up. This is a very elastic collision and has a CoR close to 1, which means that the ball bounces back close to the height from which it was dropped. In contrast, a bean bag hitting the same hard floor doesn’t bounce at all; this is a very inelastic collision and has a CoR close to 0. In their tests, the bamboo bat was held in place and a hard cricket ball was hit against it at different speeds. The speed of the ball bouncing off the bat was measured at different points and compared to a willow bat. In this way, the scientists could tell whether the bamboo bat would behave in a similar way to a wooden bat and therefore make a good replacement.
*© Cjp24, licenced through Creative Commons and accessed here - https://commons.wikimedia.org/wiki/File:Compression_test-Universal_testing_machine.jpg

## Slide 8: What did the scientists find out?
Similarities Bamboo cricket bats perform very like traditional willow bats.
Differences
Bamboo bats were heavier than willow - this makes it harder for cricketers to play certain shots.
What do you think should happen next?
Notes: Ask children: What do you think should happen next? Why?
Bamboo should be used to make cricket bats. Why? – because they is plenty of it and it grows quickly (it is a more sustainable material).
Bamboo bats should not be used to make cricket bats. Why? – because they are too heavy / because it is not allowed in cricket rules.
The bamboo bat design needs to be improved. Why? – to make the bamboo cricket bat lighter because then the cricketers can do all the shots they want and lots of new bats can be made.
Notes for teachers
At this time, the MCC have rejected the possibility of players using bamboo bats as they say that the blade of the bat must be made of wood. However, this is due to be discussed again at the next laws committee meeting and there could still be a future for bamboo cricket bats.

## Slide 9: Who were the scientists?
Ben Tinkler-Davies works in the Division of Mechanics, Materials and Design which is part of the Department of Engineering at the University of Cambridge. He is a lifelong cricketer and follower of the game.
Michael H Ramage also works in the Division of Mechanics, Materials and Design.
Darshil U Shah works in the Centre for Natural Material Innovation which is part of the Department of Architecture at the University of Cambridge. He is a passionate cricket fan.
Why do you think the scientists were interested in exploring new materials for cricket bats?
© James Bowe*
Notes: Collaborations between scientists in different departments at the same university are common and the scientists bring different knowledge and skills to the research process.
Ask the children:
Why do you think the scientists were interested in exploring new materials for cricket bats?
Their primary objective was to find a material that was more sustainable than traditional willow. Bamboo was an obvious choice to start with as it grows very quickly and can be sustainably sourced.
Useful website:
https://www.cam.ac.uk/stories/bamboo-cricket-bats
This is a Cambridge University website which explains this study on cricket bats. You might like to show the photos of the scientists to your children. The text is aimed at adults but might be suitable for some older children.
*© James Bowe, Cambridge University Department of Engineering

## Slide 11: Your turn to investigate
Can you measure the ‘bounciness’ of different surfaces?
What will you change?
What will you keep the same?
What will you measure?
Wall
Bounce back
Box
Ramp
Ball
Notes: Resources
Hard surfaces e.g., plastic, wood, a hard ball (e.g., cricket ball), ramp, chalk, measuring tape, stopwatch & calculator (optional)
Instructions
Provide a cricket ball (or a hard ball of a similar size) and a range of different materials that cricket bats could be made of.
Encourage the children to feel the surfaces. Discuss what they are made of and their properties - how bendy/stretchy are they? Ask the children to predict which surface will allow the ball to bounce furthest after the ball hits it and to suggest why.
In small groups, children roll the ball down a ramp towards a wall (or similar hard surface) so that it bounces off. Mark and measure the distance that the ball bounces back from this hard surface.
Fix different surfaces against the wall and repeat.
From their tests, children can order the surfaces according to how bouncy they are.
Depending on their age and abilities, children could repeat their measurements, take averages and present their data on a bar chart.
Some children could measure the time taken for the ball to reach the wall from the end of the ramp and the time it takes to get back to the ramp. Finding the ratio of these times would give a rough coefficient of restitution between 0 – 1.
Questions to ask the children
Can you predict which surface is most bouncy? Why do you think this?
Which surface was most/least bouncy? How do you know?
Did any results surprise you?
What was tricky?

## Slide 12: Your turn to investigate
What will you change?
What will you keep the same?
What will you measure?
Can you measure the ‘bounciness’ of different balls?
Notes: If you can’t find different surfaces to test, this is a similar investigation but varying the types of balls rather than the surface.
Resources
Hard surface, range of balls made with different materials,
ramp, measuring tape, stopwatch & calculator (older children)
Questions to ask the children
Can you predict which ball is most bouncy? Why do you think this?
Which ball is most/least bouncy? How do you know?
Did any results surprise you?
What was tricky?

## Slide 13: What did you find out?
What material do you think would be good for a cricket bat/ball?
Why do you think this?
………………… is a good material for a bat/ball* because……
…………………is not a good material for a bat/ball* because………
The best material for a bat/ball* is……. because it is……….
Notes: * Delete as appropriate according to what materials the children investigated.

## Slide 14: Questions for further learning
Think of a sport you play and the equipment you use to play it.
What are the important properties of the equipment?
How do those properties affect the choice of materials used?
Why do sporting governing bodies have rules, or laws, that participants must follow?
Can you research rules that other sports have regarding the equipment that people can use to play them?
How do the materials that the sports equipment is made of affect the way a sport is played?
Do all plastics/papers/woods/metals have the same properties?
What properties of common materials can you measure?*
What equipment will you use?
Notes: *Measuring the properties of other different materials - Resources
Variety of materials, range of measuring equipment: rulers, protractors, force meters, stop watches, data logger
Depending on the materials and measuring devices you provide, children can carry out a range of investigations.
Here are some ideas to get you started:
How squashable (compressible) are the materials? Provide sponges, play doughs – add weights and measure distance compressed.
How bendy (flexible) are the materials? Provide a range of materials that are flexible (e.g. plastic ruler) and measure distance moved with rulers or the angle of movement with protractors.
How stretchy (elastic) are the materials? Provide elastic bands, socks, tights, other fabrics – use rulers to measure the length with/without stretching. Children could compare the ratio of stretched: unstretched materials.
How strong are these materials? Provide a range of plastic bags or threads – test to destruction with weights or force meters.
How loud are these materials? Provide a range of fabrics, papers, plastic bags - test waving/shaking different materials and measure sound levels with data loggers/sound meters
Questions to ask the children
How could you alter the shape/size/appearance of this material?
Can you describe the properties of this material?
Can you measure any of the properties of this material?
How will you compare this property in different materials?
What measuring device will you need for this?
What will you measure?

## Slide 15: Cross-curricular links
Maths
Comparing and measuring distances – Measuring bounciness of different balls
Measuring time and calculating ratios (older children) - Measuring bounciness of different balls
Measuring and comparing with different units - Measuring properties of materials

## Slide 16: Cross-curricular links
Writing
Newspaper report - Write a report about bamboo cricket bats
Persuasive writing - Write a letter to MCC to persuade them to allow cricketers to use bamboo bats or make a leaflet explaining the benefits to the environment of using bamboo cricket bats
Explanation - Explain how willow and bamboo bats are similar and how they are different
Letters/poems - Write a Letter to the Earth* to express your feelings about what is happening to willow trees and other natural resources in the world
Notes: *Letters to the Earth is a collection of letters and poems which express human feeling about the climate crisis.
You can find out more about this the climate science section of our Why&How Newsletter (Issue 9) – Connecting Nature and Caring for the Earth.
To see more Why&How climate science articles, visit www.pstt.org.uk

## Slide 17
This PowerPoint is intended to be a guide for teachers for their reference although they may wish to show certain slides in the classroom.
Copyright
The materials included in these resources are ©Primary Science Teaching Trust 2021 but may be freely reproduced by teachers in schools for educational purposes, subject to the source being credited. Materials may not be used for promotional or commercial purposes without the express permission of PSTT. On no account may copies be offered for sale. Feedback
We would welcome any feedback on these materials.
Please email info@pstt.org.uk or complete this short survey.

## Slide 18
For more information on the Primary Science Teaching Trust and access to a large selection of PSTT resources, visit our website:
www.pstt.org.uk
/PrimaryScienceTeachingTrust
/PSTT_whyhow
/PSTT_whyhow