## Slide 1: Water can be harvested from the air in very dry climates
Teacher Guide
Curriculum links: Condensation and evaporation
Suitable: 7-11 years

## Slide 2: Water can be harvested from the air in very dry climates
Subject knowledge
Enquiry skills*
Understand that some materials change state when they are heated or cooled
The United Nations predicts that by 2025, 48 countries throughout the world will experience water scarcity or stress. Scientists have designed a box containing a special substance that can capture water vapour from desert air and turn it into drinkable water, just using the energy from the Sun. Children will learn about condensation and evaporation, how this happens in the natural world, and how these processes are exploited in the water harvester box.
Show that water vapour in the air condenses when it is cooled
Explore how a material (shaving gel) takes up water vapour (no change of state) and releases water vapour by evaporation when warmed (change of state)
Investigate which materials hold the most liquid water
Summary of science research
Related investigations for children
Notes: *We recommend that you focus on one of these enquiry skills when children carry out one of the research-related investigations.
Of course, you might like to choose a different focus:
Asking questions
Making predictions
Observing and measuring
Recording data
Evaluating

## Slide 3: Key vocabulary
ambient - the temperature of the surrounding environment
condense - change from a gaseous state (vapour) to a liquid
evaporate - change from a liquid into gas (vapour)
gas - no fixed volume or shape, it will completely fill its container
humidity - a measure of the mass (g) of water vapour in one cubic metre (m3) of air
liquid - fixed volume but no fixed shape, it takes the shape of its container
porous - having small spaces (pores) that can hold a gas or liquid or that will allow these to pass through
saturate - hold as much water or moisture as possible
organic - a substance that contains carbon
solid - fixed volume, fixed shape
water vapour - water in gaseous form, an invisible gas
Notes: Notes for teachers

## Slide 4: Quick activity
Can you collect water from the air you breathe?
Notes: Resources
cold mirrors, magnifying glasses
NOTE: put the mirrors in a fridge for at least an hour before this activity.
Ask children to blow on their hand – What can they feel? What can they see?
Agree that there is something in the air which can be felt but not seen.
Give children cold mirrors to breathe on – what can they see?
They should see tiny droplets of liquid water. (You might want to provide magnifying glasses to look closely).
Where has the water come from?
Water vapour from their breath has condensed on the mirror.

## Slide 5: Who were the scientists?
Professor Omar Yaghi was born in Jordan to a refugee family originally from Pakistan.
He moved to USE when he was 15 years old.
He is now a professor of chemistry at the University of California.
What challenges do you think Professor Yaghi might have faced?
Notes: When Omar Yaghi moved to USA at 15, he knew little English. He will have had to learn a new language and worked hard at school to get good exam results, then gone to university.

## Slide 6: Who were the scientists?
Professor Omar Yaghi and 8 other scientists worked on this project:
Hyunho Kim,1 Sungwoo Yang,1 Sameer R. Rao,1 Shankar Narayanan,1
Eugene A. Kapustin,2,3 Hiroyasu Furukawa,2,3 Ari S. Umans,1 Omar M. Yaghi,2,3,4 Evelyn N. Wang1
Department of Mechanical Engineering, Massachusetts Institute of Technology (MIT), USA.
Department of Chemistry, Kavli Energy NanoScience Institute and Berkeley Global Science Institute, University of California–Berkeley, USA.
Materials Sciences Division, Lawrence Berkeley National Laboratory, Berkeley, USA.
King Abdulaziz City for Science and Technology (KACST), Riyadh 11442, Saudi Arabia.
Together they wrote a paper: Water harvesting from air with metal-organic frameworks powered by natural sunlight. Published in Science 356, 430–434 (2017)
Why do you think these two countries shared their ideas and think it is important to develop atmospheric water harvesting?
Notes: Teachers could talk to children about group work:
Does everyone in a group always know the same things?
Consider the climate – ask the children:
What do you know about habitats in both the USA and Saudi Arabia?
What do you know about the climate (weather, temperatures, humidity, etc.)?

## Slide 7: What did the scientists know?
Water vapour (gas) is present in the air, even in deserts.
The amount changes at different times of day.
One third of the Earth is ‘water stressed’.
What impact does this have on plants and animals?
Notes: Water stress occurs when the demand for water exceeds the available amount during a certain period or when poor quality restricts its use.
Water scarcity can mean scarcity in availability due to physical shortage, or scarcity in access due to the failure of institutions to ensure a regular supply or due to a lack of adequate infrastructure. According to the UN website (https://www.unwater.org - accessed on 1.7.20) water scarcity will be exacerbated as rapidly growing urban areas place heavy pressure on neighbouring water resources. Climate change and bio-energy demands are also expected to amplify the already complex relationship between world development and water demand.
Questions to discuss with the children:
Which countries of the world are most likely to be ‘water stressed’?
What could cause this water stress?
How do dry, desert habitats compare with other habitats?
What is the impact on the people who live in these areas of the world?

## Slide 8: What did the scientists do?
The scientists built a water harvester box which can collect water vapour (gas) from desert air during the night and turn it into drinkable water.
Inside the box is a substance called a MOF.
MOF is made of organic substances (carbon, hydrogen) and a metal called zirconium.
Water vapour ‘sticks’ to the MOF.
To make the ‘best’ water harvester, the scientists:
compared different types of MOFs
compared different boxes
What do we mean by ‘best’ water harvester?
Notes: Questions to discuss with the children:
What do think MOF stands for?
MOF-801 is a chemical called a metal-organic framework (MOF) composed of organic substances (mostly carbon and hydrogen) and a metal.
This particular MOF has the name MOF-801 and contains the metal zirconium [Zr6O4(OH)4(fumarate)6].
Do you know anything about carbon and hydrogen?
In general, an organic compound is a substance that contains carbon. Conversely, an inorganic compound would be one that does not contain carbon.
A hydrocarbon is an organic compound consisting entirely of hydrogen and carbon. Hydrocarbons are naturally-occurring compounds and form the basis of crude oil, natural gas, coal, and other important energy sources.
Examples of carbon: graphite in pencils; diamonds in jewellery; carbon fibre objects such as tennis rackets.
Note: carbon fibres are about 5–10 micrometres in diameter and composed mostly of carbon atoms. They are very stiff, strong, light, and relatively resistant to chemical and temperature changes. These properties have made carbon fibre very popular in aerospace, civil engineering, military, and motorsports, along with other competition sports.
Examples of Hydrogen: hydrogen in one of the 2 elements of water (H2O), ammonia (NH3).
What do we mean by ‘best’ water harvester?
Possible answers:
The device that collects liquid water the quickest
The device that collect the most liquid water
The device that is cheapest to build
The device that uses the least energy

## Slide 9: What did the scientists find out?
The scientists managed to harvest 2.8 litres of water in every kilogramme of MOF each day, in the very dry climate.
More water can be harvested by using more MOF or bigger boxes.
The scientists are already testing new MOFs.
Notes: Click on the hyperlink included on this slide to watch the scientists talking about the new water harvester box works (3-minute film clip).
https://www.youtube.com/watch?v=-6T3ICXWqjc

## Slide 11: Your turn to investigate
What happens to the outside of the glass?
Can you explain what is happening using these words?
Room temperature
Cold
Particles
Condense
Condensation
Water vapour
Gas
Cool
Water
Liquid
Notes: Resources
glass, ice, water
Where does the liquid water collect?
Water vapour in the air (blue dots) condenses onto cold surfaces.
Note: some children may think that water has leaked through the glass or spilled over the sides – this is a very common misconception.
To demonstrate that this is not possible, children could compare the glass of ice-water with a glass of room temperature water.

## Slide 12: Your turn to investigate
What happens to the shaving gel?
Try this in the classroom and/or watch a time-lapse film to observe how shaving gel changes.
Which of these two processes involves a change of state?
1
Water vapour
2
Notes: Resources: plastic lid/plate, shaving gel, table lamp
This activity demonstrates 2 processes.
Click on the hyperlink to view a short time-lapse film (34 seconds) showing how shaving gel changes.
Children can try this for themselves…
1. Water vapour uptake
Place a small amount of shaving gel on the lid/plate. Watch the shaving gel as it takes up some water vapour from the air.
Explanation: The water vapour permeates the gel and becomes part of the structure of the gel. There is no chemical change here or change of state.
2. Water vapour release
Children could see how water vapour is released back into the atmosphere from the gel over time or with the heat lamp to speed things up.
Ask - Why does the gel shrink when it is heated?
Explanation: The gel itself does contain an amount of liquid water. Heat causes the liquid water within the gel to evaporate and become water vapour. There is a change of state here. The water vapour is released into the air and so the gel shrinks. After several hours there is hardly any gel. This is because most of the gel was made of water which has evaporated.

## Slide 13: What happens inside the scientists’ box?
Heat from the Sun releases the water vapour from the MOF. There are so many water vapour molecules trapped in the box that some condense as liquid water on the sides.
Water vapour ‘sticks’ to the MOF.
Notes: The 2 concepts demonstrated in Activities 1 & 2 can be brought together to explain how the box works.
Ask - what do you think happens inside the box?
This schematic diagram explains how the MOF collects the water vapour and releases it.
Water vapour ‘sticks’ to the MOF and stays there because bonds are formed between the water molecules and the MOF.
The next day, heat from the Sun warms the MOF powder and the water molecules come out of the MOF as water vapour. The Sun’s energy is needed to release the water molecules (break the bonds) sticking it to the MOF.
Enough water vapour molecules are released to fill (saturate) the trapped air and so some water vapour must condense as liquid water, even at the temperatures near that of the surrounding area. So in this case it isn’t necessary for the box to be cold. To explain saturation to children further, you could add salt or sugar to water. The crystals will dissolve at first but if you keep adding more, the water becomes saturated and the remaining salt or sugar will simply fall to the bottom of the container.

## Slide 14: Questions for further learning
How do dry, desert habitats compare with other habitats?
Children could research animals and plants living in desert regions and compare with another habitat or their local environment*.
How much water can you collect in a few minutes?
How much water would be collected in an hour?
In a day?
In a week?
In a year?
Can you think of ways to reduce the use of fresh water?
How much water is wasted from a dripping tap?
Notes: *Children could visit different locations outside: playground; parkland; garden; cemetery; sports field.
Dripping Tap activity
Resources - Dripping tap, beaker or jug, measuring cylinder if the collecting vessel does not have volume markings.
Children to measure water wasted via dripping taps (measured for a few minutes).
Then they could calculate the amount of dripping water that would be wasted in a day, a week and even yearly ‘loss’ (if the drip is not corrected).
Other possibilities:
Teachers could encourage other suggestions for investigating water wastage, e.g. also consider comparing bath vs shower use of water and smaller toilet cisterns.
Teachers might discuss use of water butts in gardens to collect rainwater instead of using fresh water supplied via taps.

## Slide 15: Cross-curricular links
Writing
Persuasive writing - Leaflet or poster to persuade people to conserve water
Diary (a day in the life of…) - A child collecting water in a water stressed country
Poem - About water stress
Geography
Find out which countries of the world are most likely to be water stressed using the United Nations interactive map.*
Research the impact on people who live in water-stressed areas.**
Maths
Capacity / Multiplication - Dripping tap calculations
Notes: *UN interactive map allows anyone to investigate the proportion of people using safe drinking water in different regions of the world. Visit - https://sdg6data.org/en/maps
Children may need support to use the UN map. It is possible to select a specific country, or a region, or the world, to display data showing % population using safely managed drinking water. You can also view data showing % population with access to drinking water on the premises, or free from contamination.

## Slide 16
This PowerPoint is intended to be a guide for teachers for their reference although they may wish to show certain slides in the classroom.
Copyright
The materials included in these resources are ©Primary Science Teaching Trust 2019 but may be freely reproduced by teachers in schools for educational purposes, subject to the source being credited. Materials may not be used for promotional or commercial purposes without the express permission of PSTT. On no account may copies be offered for sale. Feedback
We would welcome any feedback on these materials.
Please email info@pstt.org.uk or complete this short survey.

## Slide 17
For more information on the Primary Science Teaching Trust and access to a large selection of PSTT resources, visit our website:
www.pstt.org.uk
/PrimaryScienceTeachingTrust
/PSTT_whyhow
/PSTT_whyhow